## Slide 1
Making our homes fit for the future
Dr Katherine Adams
Jon Bootland
Dr Kerry Mashford OBE

## Slide 2: Jon Bootland Passivhaus Trust
Passivhaus Trust The Foundry, 5 Baldwin Terrace, London N1 7RU Tel: 0207 704 3502
Email: info@passivhaustrust.org.uk Web: www.passivhaustrust.org.uk
Passivhaus:
An introduction
Underhill House: Seymour-Smith Architects

## Slide 3
A comfort standard
From a Comfort Perspective …
Constant year round temperature (20°C)
No draughts
No overheating
No cold radiant temperature in winter (no condensation and mould growth risk)
Fresh, clean, warm air
Whole house is warm

## Slide 4
Passivhaus Trust The Foundry, 5 Baldwin Terrace, London N1 7RU Tel: 0207 704 3502
Email: info@passivhaustrust.org.uk Web: www.passivhaustrust.org.uk
A route to Net Zero

## Slide 5: An energy standard
Criteria | Passivhaus Classic | EnerPHit
Space Heating Demand | ≤ 15 kWh/m2.year | ≤ 20 or 25* kWh/m2.year
Primary Energy Demand | ≤ 120 kWh/m2.year | ≤ 120 + (QH – 15) * 1.2 kWh/m2.year
Airtightness n50 | ≤ 0.6 ach @ 50Pa | ≤ 1.0 ach @ 50Pa
Summer Overheating | Max 10% > 25°C | Max 10% > 25°C
Surface Temperature (windows) | > 17°C | > 17°C
Ventilation | 30m³/hr.person | 30m³/hr.person
* Depending on Climate Zone

## Slide 6
  Buildings
    - Through UK based certifiers
  Products / Components
    - Through Passive House Institute
    - Is a demonstration of performance but not required (except for MVHR systems)
  Designers / Consultants
    - Through CEPH courses
    - List of CEPH designers / consultants on the PH Trust website
  Tradesmen / Installers
    - Through Certified Tradesman courses
Building to Passivhaus Principles is NOT the same as building to the Passivhaus Standard!
A quality standard

## Slide 7
Developed by Dr. Wolfgang Feist and Prof. Bo Adamson in the 1980s
Over 60,000 Passivhaus projects have been completed world-wide.
  Passivhaus is now the world’s leading international low-energy standard.
  It is a building concept that can be adopted by anyone
An international Standard

## Slide 8
Passivhaus principles
Notes: Space heat demand = certified through PHPP. May still possible to certify if this figure is over 15 as long as peak heat load is 10 W/m2 or less.
Pressure test = result of test / certificate as proof.
Primary energy = certified through PHPP.
Frequency of overheating = certified through PHPP.

## Slide 9
Balanced energy use
Windows & Doors
Roof
Floor
Walls
Thermal Bridges
Infiltration
Ventilation
Internal Gains
Solar Gains
??
Heating
15 kWh/m2.year

## Slide 10
UK Passivhaus 2022
>1490 complete, > 7000 underway
passivhausbuildings.org.uk
Case studies can be viewed at: http://bit.ly/PHTprojects
Notes: All that has led to this position/ activity for PH in the UK.

## Slide 11: Also applies to refurbishment
  “Quality-Approved Energy Retrofit with Passive House Components”
  The goal was to create a standard for an economically and ecologically optimal energy retrofit, for old buildings that cannot achieve Passive House Standard with reasonable effort. (PHI)
Lena Gardens

## Slide 12
Multiple single-dwelling retrofits
e.g. Passmore Street, Grosvenor Estates
Notes: And imaginative practitioners have even persuaded leading clients to trial EnerPHit on individual dwellings, such as Passmore Street.
Although these are successful, my concerns still remain that this is not a cost-effective solution in most cases due to cost.
The reason that it worked on these schemes was because of their price (millions) and the client’s willingness to pay the additional cost of EnerPHit, as they could recoup the costs in sale value because of Passivhaus’s status as a premium/ world-leading brand.

## Slide 13
Passivhaus Retrofit 2022
Almost 100 units complete & certified
Ernerley Close the largest with 32 units
Approx 30 more underway
Notes: All that has led to this position/ activity for PH in the UK.

## Slide 14: Why choose Passivhaus?
Better Energy Performance
Greater Occupant Comfort
Comparable Capital cost
Lower running costs
Futureproof:
Passivhaus as a route to Net Zero
Quality now:
Passivhaus as a low risk approach

## Slide 15
What you actually get …
Chart: kWh/m2.a
| Average UK New Build | Average UK New Build (inc Performance Gap) | Passvihaus New Build
 | 103 | 170.98 | 19.9
 | 22.9
 | 3.2
Lighting and Electricity
Domestic Hot Water
Space Heating
73% lower

## Slide 16
2011 Measured performance
Primary Energy: 100.19 kWh/(m².yr) (Everything, including space/water heating)
Space Heating: 8.86 kWh/(m².yr)
Y Foel, the first Certified PH project in the UK
North Wales (2006/7)
Notes: This is Y Foel

## Slide 17
Chart: kWh/m2.a
| Average Existing Home | Average UK New Build | EnerPHit
 | 294 | 103 | 27.7
 | 22.9
 | 3.2
EnerPHit – reduced emissions …
48% lower
Lighting and Electricity
Domestic Hot Water
Space Heating
100m2 house = £140 p.a.
81% lower

## Slide 18
Chart: kWh/m2.a
| Initial Energy Demand | Energy Demand Post Retrofit
Example 1 | 186 | 52
Example 2 | 252 | 46
Passivhaus Retrofit
Example 1
Early 1900s solid wall semi detached 3-bed retrofitted to EnerPHit standard
Small Retrofit Examples – Primary Energy
72% reduction
Example 2
Detached 4 bed solid wall property to EnerPHit standard
82% reduction

## Slide 19: Staged Retrofit
  Allows for phased budgeting
  Allows components to be replaced as they reach end of life
  Removes the risk of Carbon Lock-in
  Enables forecasting of future potential reductions

## Slide 20
Underhill House: Seymour-Smith Architects

## Slide 21
Plummerswood, GAIA Architects

## Slide 23
Denby Dale, Green Building Store & Derrie O’Sullivan Architects

## Slide 25
Erneley Close, Manchester : 2E Architects
Passivhaus Trust The Foundry, 5 Baldwin Terrace, London N1 7RU Tel: 0207 704 3502
Email: info@passivhaustrust.org.uk Web: www.passivhaustrust.org.uk
Questions
Jon Bootland
jon@passivhaustrust.org.uk

## Slide 26
Panel discussion